Progress toward source-to-target simulation*

D. P. Grote, A. Friedman, G. Craig, W. M. Sharp, LBNL, 1 Cyclotron Road Bldg 47R0112, Berkeley, CA, 94720-8201

I. Haber, University of Maryland, College Park, MD 20742-3511

Source-to-target simulation of an accelerator provides a thorough check on the consistency of the design as well as a detailed understanding of the beam behavior.  Issues such as envelope mismatch and emittance growth can be examined in a self-consistent manner, including the details of accelerator transitions, long-term transport, and longitudinal compression.  The large range in scales, from centimeter-scale transverse beam size and applied field scale-length, to meter-scale beam length, to kilometer-scale accelerator length, poses a significant computational challenge.  The increasing computational power that is becoming available through massively parallel computers is making such large-scale simulation realizable.  This paper discusses the progress toward source-to-target simulation using the WARP[1] particle-in-cell code.  Representative examples will be shown, such as 3-D, long-term transport simulations of Integrated Research Experiment (IRE) scale accelerators.

This work performed under the auspices of the U.S Department of Energy by University of California, Lawrence Livermore and Lawrence Berkeley National Laboratories under contracts No. W-7405-Eng-48 and DE-AC03-76SF00098.

D. P. Grote, A, Friedman, I. Haber, S. Yu, “Three-Dimensional Simulations of High-Current Beams in Induction Accelerators with WARP3d,” Proceedings of the 1995 International Symposium on Heavy Ion fusion, Fusion Engineering and Design, 32-33 (1996) 193-200.